## Slide 1
POLITECNICO DI TORINO
COLLEGIO DI INGEGNERIA INFORMATICA, DEL CINEMA E MECCATRONICA
M.SC. IN MECHATRONIC ENGINEERING
ROS over the Internet:
developing a VPN-based ROS network to enable remote communication using a
3D printed robot hand
Supervisors: Prof. Paolo Prinetto
Supervisors at HotBlack Robotics:
Ph.D. Ludovico Orlando Russo
Ph.D. Gabriele Ermacora
​Author: Cesare Pecone​

## Slide 2
Developed Solution
  Robot Operating System (ROS)
  Virtual Private Network (VPN)
  Docker
Conclusions
  Future Developments
OUTLINE AND MOTIVATION
Introduction
  Robotics & Service Robots
  Cloud Computing & Cloud Robotics
The PARLOMA Project
  State of the art
  Open Issues
ROS over the Internet:
developing a VPN-based ROS network to enable remote
communication using a 3D printed robot hand

## Slide 3
ROBOTICS
  Industrial Robots
  Exploration and Scientific Robots
  Medical Robots
  Service robotics
    Agricultural Robots
    Edu-tainments Robots
I. Introduction | 1

## Slide 4
CLOUD COMPUTING
ROBOTICS
I. Introduction | 2

## Slide 5
2
CLOUD COMPUTING
ROBOTICS
‘’Humans as a species are becoming more intelligent because we are able to share information much more quickly and take advantage of innovations faster, even
robots have that potential’’ K.G.
I. Introduction | 2

## Slide 6
The PARLOMA project allows remote communication between:
two deafblind people
a deafblind person to a deaf person
deafblind person to a hearing person with a knowledge of sign language
THE PARLOMA PROJECT
3
II. The Parloma Project | 3

## Slide 7
DATA TRANSMISSION
Gestures reproduction
THE PARLOMA PROJECT
Hand Tracking
II. The Parloma Project | 4

## Slide 8
5
PARLOMA ARCHITECTURE – STATE OF ART
II. The Parloma Project | 5

## Slide 9
LAN C
?
?
LAN A
5
LAN D
Open Issues
PARLOMA ARCHITECTURE – STATE OF ART
LAN B
Local Area Network
II. The Parloma Project | 5

## Slide 10
A framework designed for robotics application developments.
Each actor involved in PARLOMA, such as I/O modules and Platform, performs within it some processes called ROS nodes.
These nodes communicate between them exchanging messages on topics.
ROBOT OPERATING SYSTEM (ROS)
output/serial_topic
Joint_command
MASTER
Node
Publisher
Node
Subscriber
Node
Input Module​
ROS Environment
on a LAN
Cloud Platform
Output Module
III. Developed Solution | 6

## Slide 11
A framework designed for robotics application developments.
Each actor involved in PARLOMA, such as I/O modules and Platform, performs within it some processes called ROS nodes.
These nodes communicate between them exchanging messages on topics.
ROBOT OPERATING SYSTEM (ROS)
output/serial_topic
Joint_command
[180, 0, 0, 0, 180] ​
MASTER
Node
Publisher
Node
Subscriber
Node
Input Module​
ROS Environment
on a LAN
Cloud Platform
Output Module
III. Developed Solution | 6
[π, 0, 0, 0, π] ​

## Slide 12
A network technology that embeds all the ROS equipped devices in the same network, assigning each of them a unique IP address, regardless their corresponding LAN.
VIRTUAL PRIVATE NETWORK (VPN)
III. Developed Solution | 7

## Slide 13
Server
Input
Client
Output Client
Necessary files to build a VPN solution:
Certification Authority
Server Certificate, Encryption Files and Server Key
Client Certificate and a Key Pair, for each client
Server configuration file
Clients configuration files
Run the service
VIRTUAL PRIVATE NETWORK (VPN)
port 1194
proto tcp
dev tun
ca ca.crt
cert server.crt
key server.key
dh dh2048.pem
server 10.8.0.0 255.255.255.0
ifconfig−pool−persistipp.txt
keepalive 10 120
tls−auth key.txt 0
cipher AES−256−CBC
persist−key
persist−tun
client
dev tun
proto tcp
remote serveripaddress 1194
resolv-retry infinite
nobind
persist−key
persist−tun
ca ca.crt
cert client_in.crt # or client_out.crt
key client_in key # or client_out.key
remote−cert−tls server
tls−auth key.txt 1
cipher AES−256−CBC
III. Developed Solution | 8

## Slide 14
VPN
PARLOMA ARCHITECTURE – VPN SOLUTION
LAN B
LAN C
LAN A
5
LAN D
III. Developed Solution | 9

## Slide 15
USER C
USER D
LAN C
LAN B
LAN D
LAN A
?
PARLOMA ARCHITECTURE
VPN
III. Developed Solution | 10

## Slide 16
An operating-system-level virtualization software that allows to run multiple application instances (containers).
DOCKER
VIRTUAL MACHINE
DOCKER
III. Developed Solution | 11

## Slide 17
FROM osrf/ros:indigo-desktop-full
RUN \
svn checkout https://github.com/creos92/parloma.git/trunk/Client &&\
svn checkout https://github.com/creos92/parloma.git/trunk/parloma_ros &&\
apt-get update &&\
apt-get install build-essential checkinstall -y &&\
apt-get install libssl-dev liblzo2-dev libpam0g-dev wget -y &&\
wget https://swupdate.openvpn.org/community/releases/openvpn-2.4.4.tar.gz &&\
sudo tar zxvf openvpn-2.4.4.tar.gz &&\
cd openvpn-2.4.4 && ./configure && make && checkinstall -y &&\
/bin/bash -c 'source /opt/ros/indigo/setup.bash && \ cd /parloma_ros && catkin_make'
CMD cd parloma_ros && chmod +rx start_c._in.sh && sync && ./start_c_in.sh
FROM osrf/ros:indigo-desktop-full
RUN \
svn checkout https://github.com/creos92/parloma.git/trunk/Server &&\
svn checkout https://github.com/creos92/parloma.git/trunk/parloma_ros &&\
apt-get update &&\
apt-get install build-essential checkinstall -y &&\
apt-get install libssl-dev liblzo2-dev libpam0g-dev wget -y &&\
wget https://swupdate.openvpn.org/community/releases/openvpn-2.4.4.tar.gz &&\
sudo tar zxvf openvpn-2.4.4.tar.gz &&\
cd openvpn-2.4.4 && ./configure && make && checkinstall -y &&\
/bin/bash -c 'source /opt/ros/indigo/setup.bash && \ cd /parloma_ros && catkin_make'
CMD cd parloma_ros && chmod +rx start_s.sh && sync && ./start_s.sh
DOCKER
Cloud Platform
Output Module
output/serial_topic
Joint_command
[π , 0, 0, 0, π ]
[180, 0, 0, 0, 180] ​
MASTER
Publisher
Subscriber
Input Module​
FROM osrf/ros:indigo-desktop-full
RUN \
svn checkout https://github.com/creos92/parloma.git/trunk/Client &&\
svn checkout https://github.com/creos92/parloma.git/trunk/parloma_ros &&\
apt-get update &&\
apt-get install build-essential checkinstall -y &&\
apt-get install libssl-dev liblzo2-dev libpam0g-dev wget -y &&\
wget https://swupdate.openvpn.org/community/releases/openvpn-2.4.4.tar.gz &&\
sudo tar zxvf openvpn-2.4.4.tar.gz &&\
cd openvpn-2.4.4 && ./configure && make && checkinstall -y &&\
/bin/bash -c 'source /opt/ros/indigo/setup.bash && \ cd /parloma_ros && catkin_make'
CMD cd parloma_ros && chmod +rx start_c._in.sh && sync && ./start_c_out.sh
ROS Environment
Over Internet
III. Developed Solution | 12

## Slide 18
PARLOMA ARCHITECTURE – DOCKER SOLUTION
USER C
USER D
LAN C
LAN B
LAN D
LAN A
III. Developed Solution | 13

## Slide 19
15
EXPERIMENTS
SINGLE - MACHINE
LOCAL AREA NETWORK
WIDE AREA NETWORK
II. Developed Solution | 14

## Slide 20
15
EXPERIMENTS
LOCAL AREA
NETWORK
WIDE AREA
NETWORK
II. Developed Solution | 15

## Slide 21
The architecture built succeeded in implementing external ROS networks, connected to different LANs.
  The architecture is:
    Highly scalable
    Multi-platform
    Robust
    Flexible
The set up is extremely simple.
CONCLUSIONS
Developed Network
IV. Conclusion| 14

## Slide 22
Deafblind people can communicate remotely with their interlocutors thanks to PARLOMA.
The architecture developed could be used for many Cloud Robotics applications.
FUTURE DEVELOPMENTS
The procedure to build the Certification Authority files, should automated
Security issues
CONCLUSIONS
IV. Conclusion | 15

## Slide 23
Thank you for your attention